1 State of the art on modeling of poroelastic coatings

1.1. Biomimetics of poroelastic coatings
show a panoramics of nature inspired surfaces concentrating especially on the one already	studied for flow control and/or drag reduction
1.1.1. Riblets
citing works on drag reduction using riblets (Luchini, Jimenez…) and explain the	physical phenomena involved such as producing a slip velocity and creating some	coherent structure at the interface
1.1.2 Permeable surfaces
show that there is some evidence that porous directional surfaces and poroelastic	surfaces can outperform riblets, show some experimental and computation evidence	of this fact
1.2. Models for natural porous surfaces
Clearly state the problem that we are trying to solve (interaction between surface and fluid).	Present what has been done (physical phenomena that can be found DNS, CFD and	experiment) and which aspect still need some research (FSI, anisotropy, multiple scale	phenomena, high Re flow, interface treatment...)
1.2.1 Drag that is function of the canopy depth, (canopy flow, flow vegetation)
Present the approach based on a variable drag coefficient used by DeLangre and	others, explain some concepts in this theory like reconfiguration, Cauchy number,	Vogel exponent etc.
1.2.2. Porous media approach through homogenization
Present the generalities of homogenization technique and show the strength of	the method and what can be solved within this theory
1.2.2.1 VANS
State of the art of the VANS equation, like inertia, deformations, turbulence?,	interface treatment?
1.2.2.2. Multiple scale expansion
Principles and application of the multiple scales expansion on porous media flow,
show the dualism with the VANS
1.3 Stability of flow over permeable surfaces (monami and honami)
Present results in the field of instabilities that develops at the interface of porous surfaces

Sia Jensen che Brugem in realtà usano homogenization ma alla fine il tensore K ha un unica componente ( lo modellano al variare di porosity) perciò forse nn è giusto includerli in tensorial approach…

Remember to talk about:
- anisotropy: the K or Cd shoul vary in space inside the coating
- interface: how to couple the two models (hai gia scritto un report…)
- multiple scales (homogenization)
- FSI (the drag term in the vans is directly generated by the equations, you have to couple some mechanical solver to this)

(Control Mortazavi)
Parla del fatto che le VANS sono state applicate in moltissimi altri ambiti, (termico, multifase, acustica,.. ) e in generale sono una teoria matura; al contrario dell’approccio canopy che nn deriva da un formalismo ma è sostanzialmente un fitting sui dati sperimentali

2 VANS
2.1 Introduction
2.1.1 Generalities of homogenizations method
2.1.2 How homogenization theory compare (paper quintard yoahan)
2.2. Definition of the averaging filter
2.3 Derivation of VANS equations for 3D incompressible fluids
2.3.? Hypothesis on the sub-grid scale stress tensor
2.4 Closure model for the drag porous term
2.5 Derivation of the closure problem for the permeability and Forchheimer tensors
2.5.? Discuss on the linear map between average quantities and macroscopic quantities

3 Drag-model sensitivity of Kelvin-Helmholtz waves in canopy flows
3.1 Introduction
3.2 Model of the canopy flow
3.2.1 The mean flow
3.2.2 Stability and sensitivity equations
3.3 Sensitivity results for the isotropic drag model
3.4 An alternate sensitivity model: accounting for the canopy anisotropicity
3.4.1 Sensitivity equations
3.5 Concluding remarks

4 Effect of the geometrical parameters and inertia on the apparent permeability tensor in fibrous porous media
4.1 Introduction
4.2 Validation and Setup
4.2.1 Computational domain
4.2.2 Numerical setup
4.2.3 Mesh convergence analysis
4.2.4 Validation on two different configurations
4.2.5 Test with larger REV’s
4.3 Microscopic solutions
4.4 The apparent permeability tensor
4.5 A metamodel for H
4.5.1 DACE sampling
4.5.2 Kriging approximation method
4.6 Concluding remarks

5 A macroscopic continuum model for flow over porous beds
5.1 Introduction
5.2 Fluid solver algorithm schema
5.3 Test cases
5.3.1 Closed cavity
5.3.2 Poiseuille flow
5.4 Concluding remarks

6 Conclusions and ideas for continuing the research